Documents:
L1. "DDR3 Design Guide". -- Cavium, Rev1. May 2013, June Curtis
L2. "DDR3 Essentials, Part 1" -- Cavium, Rev 1, Oct 2013, June Curtis
L3. "DDR3 Essentials, Part 2" -- Cavium, Rev 1, Oct 2013, June Curtis

• JECEC No. 21C, www.jedec.org

• 1.5V or 1.35V

• Topologies to connect signals in DIMM:
a) fly-by (daisy-chain with short or no stubs) – address/command/control/clock signals
Skew between clock and data/data-strobes.
Corrected by write and read leveling (by software)
b) data and data strobe siganals are connected point-to-point.
Fly-by topology is used for UDIMMs. RDIMMs use T-shape topology. This is implemented inside of DIMMs.
ODT = On-Die Termination of Data(DQ) and Data Strobe(DQS) signals. They are adjustable via software.

• Signals, 4 Groups:
a) Address / Command
A[15:0]	-- Address
BA[2:0]	-- Bank Address
CAS#	-- Column address
RAS#	-- Row address
WE#	-- Write enable
RESET#	-- Reset

b) Data / Data Strobe
DQ	-- Data
DQS_P / DQS / DQS_t	-- Positive data strobe
DQS_N / DQS# / DQS_c	-- Negative data strobe

c) Control
CS[1:0]	-- Chip select
CKE	-- Clock enable
ODT	-- On-Die Termination

d) Clock
CK_P / CK / CK_t	-- positive clock
CK_N / CK# / CK_c	-- negative clock

• Signal loads
Slew rate (V/sec) – the max rate of output voltage change (deviation from square pulse).

• 1T address mode = address / command signals are asserted for only one clock cycle.
2T address mode = ... for two cycles.
T-mode is configured via software (not via SPD field).

• DDR3 chips may be x8 or x16
64-bits (72-bits with ECC = Error Correction Code DDR3 chip) = 8 * x8 chips = 4 * x16 chips
8 byte lanes, each having 8 DQ signals + data strobes DQS / DQS#

• DDR3 are organized in ranks and DIMMs.
Ranks = a collection of DDR3 chips working as a unit and having
a) the full data width (e.g. eight x8 DDR3 chips supply 64-bits data, DIMM with one rank)
b) the same chip select, address, and control signals.
DIMM = contains 1, 2, or 4 ranks each.

• DIMM implementations
UDIMM = unregistered
RDIMM = registered (contains a register)

• DIMM may contain 1 or more TWSI (Two-Wire Serial Interface)(I2C) devices, such as SPD EEPROM.
3 SPD address lines SA[2:0]
SPD EEPROM address = DIMM-address + 0x50
T-Sensor addrss = DIMM-address + 0x18

• Raw Card versions is stored in the on-board SPD (byte 62) by DIMM manufacturer.
Wrong raw card version in the software SPD data structure may result in incorrect delay values during write leveling and causing read/write failures.

• Signal timing
For Fly-By signals, all the signals in the same group must arrive together.
For P2P signals, all the signals in the same byte lane must arrive together (DQ, DQS)
See L1:Chapter 9, ~p.71

stopped at p 112