Lion -- 10 GbE Switch

►

● (48 * 10 G) port switch or (32 * 10 G + 4 * 40 G)
● Each two ports can be boundled into a single 20 Gbps port.

▒ Port Trunking a.k.a Link Aggregation (p.356)
Multiple physical links into a single logical link.
● Up to 127 trunk groups (7-bit trunk ID)
● Up to 8 port members per trunk (LAG).
● Ucast or Mcast are load balanced using:
a) Ingress port number or Trunk ID
b) Hash based on L2, L3, and L4 header fields
c) CRC on flexible selection of header fields
● Trunking is compliant with IEEE 802.3ad standard.
● All trunk members must have the same port configuration:
a) MAC settings such as speed, flow control, ...
b) QoS
c) Policy
d) Bridge sttings (VLAN, STP, Ingress/Egress filtering)
e) Egress shaping and scheduling policy
● A packet can be forwarded to a trunk by:
a) Policy actions
b) Bridge PVE
c) Bridge FDB
d) Unicast Router engine
● Trunk Members Table:
127 rows -- one per trunk ID
8 colomns -- one per each member
Trunk Member is defined by a tuple = {device number, port number}
● Load balancing within a trunk:
member = hash[0:6] % number-of-trunk-members-in-trunk

▒ Tunneling (p. 413)
● Tunneling technologies:
a) IPv4/6-over-IPv4, with or without GRE header
b) Ethernet-over-GRE-IPv4
c) IEEE 802.1ah
d) MPLS Label Switch Path (LSP)
e) IPv4/6-over-MPLS Label Edge Router (LER)
f) Ethernet-over-MPLS Label Edge Router (LER)
● Tunnel provides a P2P virtual link between two end-points
● Tunneling protocol and passenger protocol (payload encapsulated by the tunneling protocol).
Tunneling protocols:
a) IPv4
b) GRE-IPv4
c) MPLS
Passenger protocols:
a) IPv4
b) IPv6
c) Ethernet
d) MPLS label + payload
● Tunneled packet:
| Ethernet Header | Tunneling Protocol | Pssenger Protocol | Ethernet CRC |

▒ VLAN (p. 534)
IEEE 802.1Q -- Single-tag bridging.
IEEE 802.1ad -- Provider bridging, QinQ, TR101
S-tag (Service Provider VLAN tag) = 0x8a88
C-tag (Customer bridge VLAN tag) = 0x8100