● Forwarding Information Base = Routing Table = Collection of routes

● Default Route = a Network 0.0.0.0/0

● LAN = broadcast domain

● IPv4 classes:
       Address range Left-most bits Net/ Host size
A = 0.0.0.0 ... 127.255.255.255	0-------	8/24
B = 128.0.0.0 ... 192.255.255.255	10-----	16/16
C = 192.0.0.0 ... 223.255.255.255	110----	24/8
D (multicast) = 224.0.0.0 ... 239.255.255.255	1110---
E (reserved) = 240.0.0.0 ... 255.255.255.255	11111--

● Non-routable addresses
10.0.0.0/8 (Class A)
172.16.0.0/16 ... 172.31.0.0/16 (Class B)
192.168.0.0/16 (Class C)
127.0.0.0/8 (Class A)

● Scope = an indicator of the distance to the destination network = how far the owner of some IP address is from the local host.
○ Host -- communication with itself (e.g. 127.0.0.1)
○ Link -- hosts are connected with each other on the link layer (L2). LAN, broadcast domain.
○ Universe -- a destination host can be anywhere

● Multiple addresses for a interface
Primary, secondary
Aliasing -- old concept. It was overtaken by iproute2 routing capabilities.
Unlike ifconfig, iproute2 doesn't treat aliasing devices as real and independent. Aliasing device is just a label on an address for iproute2.

Also, the old concept: To configure multiple addresses on a single NIC with ifconfig -- to define virtual devices like eth0:0, eth0:1

● Commands
$ ip address list dev eth0
$ ip address add 10.0.0.1/24 broadcast 10.0.0.255 dev eth0
NOTE: "ip" command comes from iproute2 package.

Setup two virtual addresses on the same NIC:
$ ifconfig eth1:1 192.168.1.102 netmask 255.255.255.0
$ ifconfig eth1:2 192.168.1.103 netmask 255.255.255.128

● Linux uses two routing tables:
a) Table for local addresses.
b) Table for all other routes.

● Routing Cache -- a table which maintains the results of lookups (positive and negative).
Differences between Routing Table (RT) and Routing Cache (RC):
a) RT uses subnets (aggregates of consequtive addresses).
     RC uses single IP addresses.
RT:	Destination	Next hop	Device to use
10.0.1.0/24	10.0.0.1	eth0

RC:	Destination	Next hop	Device to use
10.0.1.100	10.0.0.1	eth0
10.0.1.101	10.0.0.1	eth0

RC Garbage Collection -- cleanup the RC.
a) Synchronous (when new entry is added, memory is freed, address is classified as unreachabe (faild L3-to-L2 mapping, ...).
b) Asynchronous (timer-based cleanup)

● Neighboring Subsystem Cache

● Lookups:
For RC -- simple hash
For RT -- LPM (Longest Prefix Match) algorithm.
RT is organized as a complex mesh of data structures.

● Linux kernel uses two RTs:
a) For local routes
b) Configurable by the administrator.

● /proc
/proc/sys/net/ipv4/*

● Sources
linux/
        include/linux/*.h
        net/*.h
        net/ipv4/*.c
        core/*.c

"ip" command

References:
○ http://www.computerhope.com/unix/ip.htm
○ http://linoxide.com/linux-command/use-ip-command-linux/	-- Compare "iproute2" and "net-tools."

● Assign a IP Address to Specific Interface
# ip addr add 192.168.50.5 dev eth1

● Check an IP Address
# ip addr show

● Remove an IP Address
# ip addr del 192.168.50.5/24 dev eth1

● Enable Network Interface
# ip link set eth1 up
# ip link set dev eth0 up

● Disable Network Interface
# ip link set eth1 down
# ip link set dev eth0 down

● Check Route Table?
# ip route show

● Add Static Route
# ip route add 10.10.20.0/24 via 192.168.50.100 dev eth0

● Remove Static Route
# ip route del 10.10.20.0/24

● Add Default Gateway
# ip route add default via 192.168.50.100

● Change device flags
# ip link set dev eth0 promisc on
# ip link show dev eth0

● Change MTU
# ip link set dev eth0 mtu 1412

● Change device name from ethX to mydevX
# ip link set dev eth0 name mydev

● Clear Route Table?
# ip route flush

● Monitor changes in the routing?
# ip monitor route
# ip monitor