OCTEON-SDK-based Platform Software
Development Flow and Software Releases
• Specification •

Version:	1.0.0-3
Date:	02-October-2014
Author:	Y.Tolstov

Contents

1. Terminology and Definitions
2. Software Components and Deployment Diagram
3. Software Development and Release Flow
4. Policies and Conventions
5. Software Release Procedure
6. Initial Software installation Procedure

1. Terminology and Definitions

• IMT = Interface Masters Technologies

• Platform Software = Bootloader + Simple Executive (SE) + Linux runtime environments generated from Cavium's OCTEON SDK. This software includes those modules, which are already part of the SDK (as they coming from Cavium) or additional software created by Interface Masters to make a particular OCTEON-based board operational and running SE or Linux runtime environments. This way, all application-level software, software framework, middleware, or any device driver, which doesn't follow the software model imposed by the SDK and not using its build system, are not considered being a part of the Platform Software. Differently – the Platform Software is SDK-dependent and SDK-framed.

• Base Software Release = The Software release with major functional changes or changes in the runtime environment. Such releases issued with new major or minor versions being incremented. The last digit in the version ID equals 0. Examples: 1.0.0, 2.0.0, 2.1.0, 3.0.0, ... The base releases are generated from the main development trunk for specific version of SDK.

• Maintanance Software Release = The Software release with minor functional changes or bug fixes. In such releases, only the last digit of the version ID is incremented and such releases. Examples, 2.1.1, 2.1.2, ... Such releases are generated from the maintainance branches.

2. Software Components and Deployment Diagram

2.1. Due to Cavium policy the OCTEON-SDK is never distributed to custmers by IMT.. They suppose to get it directly from Cavium. The IMT generated software releases are always tied to specific version of OCTEON-SDK.

2.2. Release Components
1. Bootloader = U-Boot – Provided in form of archived binary file(s).
2. Host Utilities = OCTEON Host utilities to operate with OCTEON over PCIe bus (64-bit only).
3. Linux = OCTEON Linux, Initial FS, and RootFS images provided in form of archived binary file(s).
4. Patch for OCTEON-SDK-x.y.z – Provided in form of a Patch for a Host required by the SDK (e.g. RedHat/CentOS).

Every new release requires building all components above from which, later, specific distribution sets may be created for IMT internal use or for shipping them to customers.

2.3. Deployment Diagram
1. The component file naming follows the General Release File Naming Format (See Ch. 4).

2. IMT Patch, normally, includes all changes for all products available in the SDK at the moment of Patch release. In some cases, Patches may be provided for a portion of SDK or for specific IMT products only.

NOTE: Here for clarity, particular versions of SDK, IMT product, and IMT releases are used.

3. Software Development and Release Flow

1. The version of OCTEON-SDK from Cavium is installed on the master branch of the OCTEON-SDK Storage (Git repository) in the original form as it is provided by Cavium (e.g.as a collection of RPM, encrypted archives, patches, files and so on). After installation and importing the SDK into the Git repository, the release is taged as SDK-x.y.z, where x.y.z is the OCTEON-SDK release version as labeled by Cavium. Note, the tag normally contains full SDK version, including build and patch numbers. If the tag consists only base version (major.minor.bugfix), then all other details (build and patch numbers should be provided in the tag description).

2. The version of OCTEON-SDK adapted to IMT needs (e.g. some pruning/cleanup or directory tree reorganization) and made from the original SDK setup (installed based on the SDK installation procedure provided by Cavium), is imported to the dedicated set of repositories on the vendor branch, on top of the previous version of SDK, and tagged as SDK-x.y.z the same way as described in 1.
NOTE, that the OCTEON-SDK modification should not reorange/change fundamental SDK structure, because, this adapted version will be compared against the original SDK during generating SDK patches.

3. All development will be performed on the master branch, which is synchroniized with the sdk-x.y.z-im branch originated from the SDK-x.y.z tag at the points of the new software releases. Note, that the sdk-x.y.z branch will be served as a main development trunk for the old version of OCTEON-SDK, after new SDK is imported into the repository.

4. Normal work flow is used, with feature branches, etc.

5. The master branch serves as a main development trunk for for the most recent SDK. For all previous versions of SDK the the appropriate SDK-x.y.z-im branches would be served as main development (more properly, the main maintanance) trunks. That requires -- before new SDK version is imported into the repository, all modifications on the master branch must be transferred to the SDK-versio-specific IMT branch.

6. When a new Release with version m.n.r needs to be generated, two scenrio are possible depending on the release type:
a) Base Release: The Release is generated from sdk-x.y.z-im branch and Base Release tag SDK-x.y.x-IM-m.n.0 is applied to that branch. Note, if the master branch is the main development trunk for the current SDK version, then prior to generating the Release and applying the Tag, the latest code from the master branch should be merged to sdk-x.y.z-im.
b) Maintanance Release: If doesn't exist yet, the maintnance branch sdk-x.y.z-im-m.n.0 for required Base Release is created -- forked from the sdk-x.y.z-im branch at the point of SDK-x.y.x-IM-m.n.0 tag. Necessary changes are performed on this branch, the Release is generated from the latest commt, and the release tag SDK-x.y.x-IM-m.n.r is applied.

7. Release component names follow the convention of software release file naming (see Ch.4). In the cosidered case, it will be, for example, imt-1.0.0.octeon-sdk-3.0.1.n804.patch (for N804 only) or imt-1.0.0.octeon-sdk-3.0.1.patch (for all boards and software modules) will be release names for the SDK patches.

The Software Development flow diagram

4. Policies and Conventions

1. The software releases (patches) are performed by the Release Engineer or dedicated software developer (not by random people and nobody outside of the software group).

2. The release procedure (see chapter 5) is automated as much as possilbe.
The procedure itself (as a set of documents, scripts, and utilities) is versioned and maintained in the source control tool.

3. The same branches and tags are created (atomically) in all OCTEON-SDK related repositories (even though there may be no changes done in some of them).
Git branch names use lower case letters and tags – capital letters.

4. The release file name format follows the Generic Software Release file name format
See this IMT Wiki page: https://50.0.45.248/mediawiki/index.php/SW:Conventions_and_Policies

5. The software release version always uses its full form recorded, as a minimum, in the release notes. The release archive may figure partial version forms.

6. The software release is distributed to customers/users in form of single tgz-encrypted file.

5. Software Release Procedure

The procedure describes:
a) How to setup the SDK, software sources, and build enviornment.
b) How to generate the components of the target Platform Software release.
c) How to perform versioning, branching, and tagging.

5.1. The procedure should not contradict the OCTEON-SDK organization ans usage described on these Wiki pages
https://50.0.45.248/mediawiki/index.php/OCTEON-SDK_Organization
https://50.0.45.248/mediawiki/index.php/OCTEON-SDK_Sources_and_Usage

5.2. Every generated release component should contain full version (e.g. 1.0.0-3 vs. partial 1.0.0 or 1.0) and follow the format described on this Wiki page:
https://50.0.45.248/mediawiki/index.php/SW:Conventions_and_Policies

5.3. Main Approaches:
1. All modifications of the OCTEON-SDK repositories, necessary for Releases, such as merging, branching, or tagging, are performed by Release Engineer on his own Workstation and then changes are pushed to the shared Git repositories. Build scripts do not perform any changes on the repositories from which they generated Releases (no automatic merging, branching, or tagging). The Build Server works in "read-only" mode regarding the OCTEON-SDK repositories.

2. The Build Scripts running on the Build Server generates the OCTEON Release Components on the Release Tag baseline.

5.4. Here, the Procedure describes main steps only. The actuall procedure is implemented as a (set of) build scripts and should be automated as much as possible.

Step 1: Perform proper branching and merging in the OCTEON-SDK repositories
The main principles of Release manangement are provided in Chapter 3.
The Release Engineers clones the full set of OCTEON-SDK repositories on his Workstation (using octeon-sdk-clone.sh script),
$ octeon-sdk-clone.sh full OCTEON-SDK
... performs necessary preparation for the release -- merging, branching, and tagging.
When done -- pushes the changes into the Central Git Repositories.

NOTE 1: All repositories, which constitute the OCTEON-SDK set, should be synchronized (branch and tag names, latest commits on all release branches).

NOTE 2: It is important, that at this point all relevant repositories have the appropriate Release Tag being applied, because, in Step 2 the build will be performed based on that Tag.

Step 2: Install OCTEON-SDK on the Build Server and generate the Release
On the Build Server:
1. Clone the full set of OCTEON-SDK repositories from the Central Git repository (with all those changes done in Step 1) using octeon-sdk-clone.sdk.sh script (the same way how it was done by the Release Engineer on his Workstation)
$ octeon-sdk-clone.sh full OCTEON-SDK

2. Generate the following Release components (see Chapter 2) on the Release Tag level:
a) Bootloader
b) Linux = Kernel + Initial FS + Root FS
... and store the generated images in some temporary directory (to avoid removing them during SDK cleanup).
NOTE: Be sure that the proper OCTEON processor type is used for the target hardware (e.g. CN66XX)
$ source OCTEON_MODEL_CN66XX

3. Clone the original Cavium distribubution of the OCTEON-SDK and set it up using the SDK installation procedure provided by Cavium.

4. Perform necessary cleanup and modifications in both SDK Setups (Original SDK and IMT-adapted-SDK). NOTE: The IMT-adapted-SDK should be checkout on the Release Tag level.

5. Generate the SDK Patch by comparing two SDK Setups.

6. Test the generated Patch.

7. Assemble all Release components (Bootloader, Linux, and SDK Patch) into a single Release Archive.

8. Move the generated Release Archive to the Software Release Storage/Server.

Step 3. Postprocessing
The goals of this step are:
1. Record all necessary information about the Release with the purpose of being able to recreate it in the future.
2. Create the Release Notes document.

6. Initial Software Installtion Procedure

TBD.
The procedure describes:
a) How to install the Platform Software on the OCTEON-based product.
b) How to setup SDK and apply the SDK patch.