Interface Masters Technologies
Notes

-------------------------------------------------------------------------------------------------------------------------------
16-February-2014, Sn
-------------------------------------------------------------------------------------------------------------------------------
[T1] Kubuntu Desktop as a Router
Environtment:
2 interfaces:
WAN = eth0
Router = 192.168.1.1, Network = 192.168.0.0/22
LAN = eth1
Router = 172.16.0.1 (Desktop itself), Network = 172.16.0.0/24
DHCP (on Desktop, eth1) range = 100...200

Setup:
1. Interfaces:
/etc/network/interfaces
Do not mention eth0 – It will be managed by the Network Manager (NM).
eth1 – static, 172.16.0.1
-------------------------------------------------------------------------------
# interfaces(5) file used by ifup(8) and ifdown(8)
auto lo
iface lo inet loopback

# eth0 = WAN interface.
# It is managed by the Network Manager (see NM configuration files)
# auto eth0
# iface eth0 inet dhcp

# eth1 = LAN interface
auto eth1
iface eth1 inet static
   address 172.16.0.1
   netmask 255.255.255.0
   broadcast 172.16.0.255
   gateway 172.16.0.1

# Make iptables rules being persistent.
post-down iptables-save > /etc/iptables.rules
pre-up iptables-restore < /etc/iptables.rules
-------------------------------------------------------------------------------
# service networking restart

2. Disable Network Manager:
/etc/NetworkManager/NetworkManager.conf
managed = false
# service network-manager restart

-------------------------------------------------------------------------------
[main]
plugins=ifupdown,keyfile,ofono
dns=dnsmasq
no-auto-default=00:14:d1:fa:18:c0

[ifupdown]
managed=false
-------------------------------------------------------------------------------

3. DHCP:
# apt-get install isc-dhcp-server
/etc/default/isc-dhcp-server
-------------------------------------------------------------------------------
# Defaults for isc-dhcp-server initscript
# sourced by /etc/init.d/isc-dhcp-server
# installed at /etc/default/isc-dhcp-server by the maintainer scripts

#
# This is a POSIX shell fragment
#

# Path to dhcpd's config file (default: /etc/dhcp/dhcpd.conf).
DHCPD_CONF=/etc/dhcp/dhcpd.conf

# Path to dhcpd's PID file (default: /var/run/dhcpd.pid).
#DHCPD_PID=/var/run/dhcpd.pid

# Additional options to start dhcpd with.
#	Don't use options -cf or -pf here; use DHCPD_CONF/ DHCPD_PID instead
#OPTIONS=""

# On what interfaces should the DHCP server (dhcpd) serve DHCP requests?
#	Separate multiple interfaces with spaces, e.g. "eth0 eth1".
INTERFACES="eth1"
-------------------------------------------------------------------------------

/etc/dhcp/dhcpd.conf
-------------------------------------------------------------------------------
#
# Sample configuration file for ISC dhcpd for Debian
#
# Attention: If /etc/ltsp/dhcpd.conf exists, that will be used as
# configuration file instead of this file.
#
# The ddns-updates-style parameter controls whether or not the server will
# attempt to do a DNS update when a lease is confirmed. We default to the
# behavior of the version 2 packages ('none', since DHCP v2 didn't
# have support for DDNS.)
ddns-update-style none;
default-lease-time 600;
max-lease-time 7200;

# If this DHCP server is the official DHCP server for the local
# network, the authoritative directive should be uncommented.
#authoritative;

# Use this to send dhcp log messages to a different log file (you also
# have to hack syslog.conf to complete the redirection).
log-facility local7;

# option definitions common to all supported networks...
option domain-name "example.org";
option domain-name-servers 208.201.224.33, 8.8.8.8;
option routers 172.16.0.1;
option subnet-mask 255.255.255.0;
option broadcast-address 172.16.0.255;

# "ytolstov" subnet
subnet 172.16.0.0 netmask 255.255.255.0 {
  range 172.16.0.100 172.16.0.200;
}
-------------------------------------------------------------------------------

# service isc-dhcp-server restart

4. IP forwarding:
# iptables -t nat -A POSTROUTING -o eth0 -j MASQUERADE
/etc/sysctl.conf	<= net.ipv4.ip_forward = 1
# sysctl -p