▒ SDK for target system using StrataSwitch and StrataXGS devices.

▒ Modular organization:
● Bootloader = CFE (not part of the SDK)
    BSP
● OS
● System Absraction Layer API = SAL
● Stacking software (BCMX layer)
● Sample Applications (Diag Shell | BCM)
● SOC = Switch-on-Chip = Internal interface which provides: device access, DMA routine, interrupt hadlers.
    POSIX-complient.
● BCM API = Absracts control of the switches and isolates the application software from hardware.
    BCM controls individual devices.
    BCM API is implemented on top of SOC API.
● BCMX API = Carries out functions on the system level.
    BCMX is built on top of BCM.
● Drivers for PHYs
    Device access: MII
● SAL = System Abstruction Layer = Library, isolates device drivers (BCM, BCMX, SOC) and Applications from system dependencies.
    SAL consists of two layers: Core SAL API and Application SAL API.
● CM = Configuration Manager
● CINT = Interactive and Script Language Interpreter.
● Bcom Protocol Stack =
   Regarded as Application because it is built on top of BCM.

~~~~~~~
  BCMX
---------
  BCM
---------
  SOC
---------
  Hardware
~~~~~~~

▒ Unlike Fiber SFPs, Copper SFPs have builtin PHY devices.

▒ Makefile hierarchy and build:
BLDDIR = ${SDK}/build/${TARGET}${target_suffix}
gmake TARGET=<targetbase>-<targetplatform>
Calling:
1. Local Makefile
2. Make.config
3. Make.tools
4. Make.local (if exists)
5. Makefile.${TARGET}
6. Make.lib
7. Make.depend

▒ Source directory layout:
build/	-- generated objects come here
include/
appl/
bcm_int/
bcmx/
customer/
sal/
shared/
soc/
make/	-- makefile infrastructure
rc/	-- Sample scripts for BCM
src/	-- System-independent sources of BCM SDK.
appl/
bcm/
bcmx/
customer/
sal/
shared/
soc/
system/	-- System-dependent sources.
bde/	-- Device enumerator
drv/	-- Device Drivers
linux/	-- Linux code
sim/	-- Simulator Platform code
vxworks/	-- VxWorks BSPs
tools/	-- Sources of some tools to build BCM.