Documents:
L1. "DDR3 Design Guide". -- Cavium, Rev1. May 2013, June Curtis
L2. "DDR3 Essentials, Part 1" -- Cavium, Rev 1, Oct 2013, June Curtis
L3. "DDR3 Essentials, Part 2" -- Cavium, Rev 1, Oct 2013, June Curtis

• Terminology
Skew = the offset in arrival time between DQ/DQS and Address/Command/Control/Clock signals.
It is measured in units of time (e.g. 120 psec).

Slew = the change of signal voltage over time.
It is measured in V/nsec.
It is important in adjusting signal drive strength and termination.

• JECEC No. 21C, www.jedec.org

• 1.5V or 1.35V

• Topologies to connect signals in DIMM:
a) fly-by (daisy-chain with short or no stubs) – address/command/control/clock signals
Skew between clock and data/data-strobes.
Corrected by write and read leveling (by software)
b) data and data strobe siganals are connected point-to-point.
Fly-by topology is used for UDIMMs. RDIMMs use T-shape topology. This is implemented inside of DIMMs.
ODT = On-Die Termination of Data(DQ) and Data Strobe(DQS) signals. They are adjustable via software.

• Signals, 4 Groups:
a) Address / Command
A[15:0]	-- Address
BA[2:0]	-- Bank Address
CAS#	-- Column address
RAS#	-- Row address
WE#	-- Write enable
RESET#	-- Reset

b) Data / Data Strobe
DQ	-- Data
DQS_P / DQS / DQS_t	-- Positive data strobe
DQS_N / DQS# / DQS_c	-- Negative data strobe

c) Control
CS[1:0]	-- Chip select
CKE	-- Clock enable
ODT	-- On-Die Termination

d) Clock
CK_P / CK / CK_t	-- positive clock
CK_N / CK# / CK_c	-- negative clock

• Signal loads
Slew rate (V/sec) – the max rate of output voltage change (deviation from square pulse).
Drive strength: Due to heavy load, the slew rate would be slow, reducing the setup margin. 2T mode is recommended to improve set and hold margins.

ODT depends on operation (read or write), the load, the DQ/DQS drive strength.
The memory architecture (number of DIMMs, DIMM types and configuration) will affect the drive strength and ODT values.

• Address modes:
1T address mode = address / command signals are asserted for only one clock cycle.
2T address mode = ... for two cycles.
T-mode is configured via software (not via SPD field).

• DDR3 chips may be x8 or x16
64-bits (72-bits with ECC = Error Correction Code DDR3 chip) = 8 * x8 chips = 4 * x16 chips
8 byte lanes, each having 8 DQ signals + data strobes DQS / DQS#

• DDR3 are organized in ranks and DIMMs.
Ranks = a collection of DDR3 chips working as a unit and having
a) the full data width (e.g. eight x8 DDR3 chips supply 64-bits data, DIMM with one rank)
b) the same chip select, address, and control signals.
DIMM = contains 1, 2, or 4 ranks each.

• DIMM implementations
UDIMM = unregistered
RDIMM = registered (contains a register)

• DIMM may contain 1 or more TWSI (Two-Wire Serial Interface)(I2C) devices, such as SPD EEPROM.
3 SPD address lines SA[2:0]
SPD EEPROM address = DIMM-address + 0x50
T-Sensor addrss = DIMM-address + 0x18

• Raw Card versions is stored in the on-board SPD (byte 62) by DIMM manufacturer.
Wrong raw card version in the software SPD data structure may result in incorrect delay values during write leveling and causing read/write failures.

• Signal timing
See L1:Chapter 9, ~p.71
For Fly-By signals, all the signals in the same group must arrive together.
For P2P signals, all the signals in the same byte lane must arrive together (DQ, DQS)
In typical design, the propagation dealy for CK is longer than for DQ/DQS. In this case, the calculated delays (during leveling procedures) are gradually increasing.

• Write Leveling – a procedure (2-step process) to calculate the delay for each byte lane.
See L2:p.29.
Step 1: Hardware write leveling. Goal – to determine the dalay with less than one clock granularity rounded to the nearest 1/4. After this the read leveling is performed.
8 tests are performed for each byte lane, in each delaying DQS in 1/8 clock increments (starting 0 * 1/8 and ending 7 * 1/8) and sampling CK (fed back on DQ bus) on the rising edge of DQS. The results are stored (in Memory Controller) in bitmasks (one for each lane): from test 0 in bit 0 till test 7 in bit 7. The goal – to find a transition from 0 to 1.

Step 2: Software write leveling. Goal – to make final adjustment to the delays determined during hardware leveling, using infromation about the toplogy (e.g. UDIMM vs RDIMM, and DIMM positions in the chain). It fixes the upper bits of the delays. This may be necessary, if delay is equal or greater than a whole clock cycle.

• Read Leveling – a 2-step procedure to adjust the delay between CK and DQx.
See L2:p.47.
Unlike Write Leveling, where the delay is the difference between propagation of CK vs. DQx, in Read Leveling, the delay is the time between RD command (sent to DDR) and data (from memory) being ready on the bus, minus the read latency (RL).
Step 1: Hardware Read Leveling:
The includes the test of 64 different delays at 1/4 clock intervals (total range of 16 CK cycles), starting at RL-1. The data bits are ORed and certain patterns are tested. Result = 1 = success, 0 = failure. The Memory Controller (MC) creates a 64-bit bitmask with results of read leveling. Bit 0 corresponds to dealy = 0 * 1/4.
The MC will look for the longest run of consecutive ones to calculate the best delay.
The leveling test is performed for different combination of RTT and ODT for each rank.
Step 2: Software Read Leveling:

stopped at L2, p.???