BCM56850

▌ Non-blocking Switch (104 * 10 GbE or 32 * 40 GbE). L2/L3 switching.

▌ Devices:
BCM56852/56853/56854/56855

▌ 32 Warpcore, each with 4 * 10 G SerDes and associated PCS, supports SGMII, XFI, XAUI, XLAUI, Bcom HiGig2, 10GBASE-KR/CR/SR, 40GBASE-KR4/CR4.
4 * SerDes lanes per Warpcore.
Single-lane (HG[11]), Two-lane (HG[21]), and Four-lane (HG[42]) configurations.

▌ Software: compatibel with StrataXGS.

▌ FCoE = Fibre Channel over Etherent.

▌ Configurations and Interfaces (see p.40)
1 GbE, 10 GbE, 20 GbE, and 40 GbE.
10/100/1000 MbE = SGMII + External PHY
1 GbE = SGMII, 1000X
2.5 GbE = SerDes
10 GbE = KR, SR, SFI, XFI, RXAUI, XAUI, KX4, CX4
20 GbE = KR2, DXAUI
40 GbE = XLAUI, KR4, CR4, SR4, XLPPI

▌ Terminology:
● VPLAG = Virtual Port Link Aggregation Group.
● VxLAN =
● L2GRE =
● NVGRE =
● MPLS =
● VPLS =
● ISATAP =
● Q-in-Q =
● TSC = TDM SerDes Core

▌ Load balancing:
Destination Module Flow Control
ECN
Dynamic Load Balancing
Enhanced Trunk Hashing
RTAG7
Symmetric Hash
Flex Hash
Resilient Hash

▌ Jambo frames up to 12K

▌ Scheduling:
SP
RR = Round Robin
WRR
WDRR

▌ Modules:
Warpcore -- 32
10/40 GbE MAC
FCoE Forwarding Engine
Packet Buffer
VLAN
L2 Processing
L3 Processing
VM Switching
Content-Aware Engine
▌ L2 Switching
Packet sizes: 64...1522 bytes (IEEE 802.3), jambo up to 12 K.

▌ VLAN
MAC-based VLANs
Protocol-based VLANs
IP-subnet-based VLANs
Port-based VLANs

▌ 40 GbE = SR Fiber or Twinax Copper

▌ Warpcore = Physical Layer interface to BCM56850 which supports up to 42 Gbps.
● Line rates = 1 GbE, 2.5 GbE, 10 GbE, 40 GbE, HG[11], HG[21], HG[40], HG[42].
● Each Warpcore contains 4 SerDes lanes. Each lane operates at 1.25 Gbps ... 10.9375 Gbps.
● Each Warpcore lane can be configurated as a single individual port or multiple lanes can be aggregated into a single port.
● MAC <=4=> SerDes Warpcore (TSC4 | 4 * Lanes) <=4=> Serial Data In/Out

▌ Device Management
● PCIe
● MIIM (IEEE 802.3u), two-wires = MDC (clock) + MDIO (bidirectional data).

▌ Packet flow:
Line
-----------
Warpcore
-----------
MAC
-----------
XLPORT
-----------
Egress/Ingress pipeline
-----------
CPU

▌ Table Lookup (p.59)
Three types of search algorithms:
● Hash Search Lookup -- For L2 MAC, L3 IP (IPv4 and IPv6), MAC VLAN, IPMC.
● Direct Index Lookup -- For VLAN and Port search (16K tables).
● TCAM (Ternary Content-Addressable Memory) Search Lookup
TCAM search examines every entry in a table simultaneously using wildcards/masks.
CAM = storage location determined not by addess, but by the content/data itself. This type of memory is parallel by its nature.

▌ Link Aggregation Group (p.312, p.422)
Allows several ports to be bundled together to form a single logical link (or trunk).
Up to 1024 LAG groups, each having up to 256 member ports.
Hardware-based LAG failover.

● VPLAG (Virtual Port LAG) = allows to group VMs into virtual LAG.
All members of VPLAG share the same IP and MAC for data plane and each having its own IP and MAC for manangement plane.

▌ NAT (p.403)
NAT (Network Address Translation) maps IP (and, possibly, ports) from one address domain to another (e.g. WAN <=> LAN).
Private IP ranges:
10.0.0.0/8
172.16.x.x/12
192.168.x.x/24
● SNAT (Source-to-Dest, outband traffic), DNAN (Dest-to-Source, inband traffic) translation.

Two variations of Traditional NAT:
● Basic NAT = NAT router modifies the IP addresses. One-to-one translation.
● NAPT

● Traditional NAT allows only Internal hosts to initiate the comm. sessions.
Bidirectional NAT allows external hosts to initiate sessions with internal hosts. B-NAT is also referred as port forwarding.

● Twice NAT = a variation of NAT in which both SIP and DIP are modified as a packet crosses the address domains/realms. Note, in Traditional NAT, only SIP[:SPO] is modified.
Use case for Twice NAT -- merging subnets with overlapping addresses.

● Subnet-based NAT = replaces only subnet portion of IP leaving the host IP as is.

● Static or Dynamic NAT (REF 2663).