From "DDR3 Design Guide". -- Cavium, Rev1. May 2013, June Curtis

• JECEC No. 21C, www.jedec.org

• 1.5V or 1.35V

• Topologies to connect signals in DIMM:
a) fly-by (daisy-chain with short or no stubs) – address/command/control/clock signals
Skew between clock and data/data-strobes.
Corrected by write and read leveling (by software)
b) data and data strobe siganals are connected point-to-point.
Fly-by topology is used for UDIMMs. RDIMMs use T-shape topology. This is implemented inside of DIMMs.

• Signals, 4 Groups:
a) Address / Command
b) Clock
c) Control
d) Data / Data Strobe

Notation:
A[15:0], BA[2:0], CAS#, CS[1:0], RAS#, WE#	-- address + control
DQ	-- data
CK_P / CK / CK_t	-- positive clock
CK_N / CK# / CK_c	-- negative clock
DQS_P / DQS / DQS_t	-- positive data strobe
DQS_N / DQS# / DQS_c	-- negative data strobe

• DDR3 chips may be x8 or x16
64-bits (72-bits with ECC = Error Correction Code DDR3 chip) = 8 * x8 chips = 4 * x16 chips
8 byte lanes, each having 8 DQ signals + data strobes DQS / DQS#

• DDR3 are organized in ranks and DIMMs.
Ranks = a collection of DDR3 chips working as a unit and having
a) the full data width (e.g. eight x8 DDR3 chips supply 64-bits data, DIMM with one rank)
b) the same chip select, address, and control signals.
DIMM = contains 1, 2, or 4 ranks each.

• DIMM implementations
UDIMM = unregistered
RDIMM = registered (contains a register)

• DIMM may contain 1 or more TWSI (I2C) devices, such as SPD EEPROM.
3 SPD address lines SA[2:0]
SPD EEPROM address = DIMM-address + 0x50
T-Sensor addrss = DIMM-address + 0x18

stopped at p 38.